## Slide 1
Adafruit ESP32 Feather (Arduino)
pH sensor at 99
EC sensor at 100
RTD sensor at 102
TRI-PMP-BX
PMP1 at 56 (pH Up)
PMP2 at 57 (pH Down)
PMP3 at 58 (EC Up)
Raspberry Pi 4 Model B Rev 1.5
DHT sensors for all zones
Automated lighting schedule
InfluxDB Cloud (Database)
org = Ethan
bucket = Test
url = https://us-east-1-1.aws.cloud2.influxdata.com
token
dht_sensors
Zone
Temp (C and F)
Humidity (%)
Datetime
water_sensors
pH
EC
RTD
Datetime
Grafana Cloud (Dashboard)
Zones 1-3
Water Reservoir
influxdb_client Python package
Built-in Compatibility
Key | 
 | Wired
 | Wireless

## Slide 2
Adafruit ESP32 Feather (Arduino)
pH sensor at 99
EC sensor at 100
RTD sensor at 102
TRI-PMP-BX
PMP1 at 56 (pH Up)
PMP2 at 57 (pH Down)
PMP3 at 58 (EC Up)
Raspberry Pi 4 Model B Rev 1.5
DHT sensors for all zones
Automated lighting schedule
InfluxDB Cloud (Database)
org = Ethan
bucket = Test
url = https://us-east-1-1.aws.cloud2.influxdata.com
token
dht_sensors
Zone
Temp (C and F)
Humidity (%)
Datetime
water_sensors
pH
EC
RTD
Datetime
Grafana Cloud (Dashboard)
Zones 1-3
Water Reservoir
influxdb_client Python package (v1)
v3 would not function on Pi
Built-in Compatibility
Evaluates and adjusts water conditions every 60 seconds.
5.5 ≤ pH ≤ 6.5
1000 ≤ EC ≤ 2000 *
Constantly reads sensor data and passes values to serial monitor.
Reads all DHT sensors and uploads values to InfluxDB.
Reads all Arduino sensor values from serial monitor and uploads to InfluxDB.
Maintains 8AM to 8PM lighting schedule.
Executed by cron every 60 seconds.
cron verifies and adjusts lighting state every 1 hour.
Query data with Flux syntax.
Key
wired_to_pi.ino
DHT_upload.py
water_upload.py
automated_lights.py
crontab